## Slide 1: Interfacing Arduino and Python

## Slide 2: Import
import in python is similar to #include<header_file> in C/C++.
Python modules can get access to code from another module by importing the file/function using import.
import serial
import time
This imports the header file to use the serial functions.
This imports the header file to use time related functions.

## Slide 3: serial.Serial
Syntax:
variable = serial.Serial ('com port', baud rate)
This is to set the baud rate and the com-port number for the serial communication from python code on your pc to Arduino or vice versa.

## Slide 4: .encode()
Syntax:
string_name.encode()
In Python 3.0, strings are stored as Unicode,
For efficient storage of these strings, they are converted into a continuous set of bytes. The process is known as encoding.
There are various encodings present which treats a string differently. The popular encodings being utf-8, ASCII, etc.
NOTE: ASCII, Unicode are different types in which characters are stored.

## Slide 5: time.sleep()
Syntax:
time.sleep(time_in_seconds)
Python's time module has a handy function called sleep().
Essentially, as the name implies, it pauses your Python program.
time.sleep() is the equivalent to the delay() function in Arduino.

## Slide 6: Some additional functions…
The readline method reads one line from the file and returns it as a string.
The string returned by readline will contain the newline character at the end.
Serial_variable.readline()
variable.split(‘character’)
At some point, you may need to break a large string down into smaller chunks, or strings. To do this, you use the split function.
What it does is split or breakup a string and add the data to a list using a defined separator.
Serial_variable.write(string_variable.encode())
The .write() function is used to write a string to the serial.

## Slide 7: Some additional functions in Arduino…
Syntax:
string_variable = Serial.readStringUntil(delimiter);
Delimiter is a condition until which the string is read and the rest of it is left out.
.readStringUntil()
.toint()
Syntax:
int_variable = s1.toInt();
toint() converts the data received into int data type.

## Slide 8: Let’s do a task…
Send two integers from python to Arduino. Check the received values and toggle the on-board LED if they are correct.
Send the values back to python serial from Arduino and print the received values in python terminal.

## Slide 9: Python code for task
import serial
import time
ard = serial.Serial('com3',9600); #serial variable
while True:
a=5
b=12
s=str(a)+";"+str(b)+".“ #convert int into string and append
ard.write(s.encode()) #writing string to serial
time.sleep(0.1) #delay
ar=ard.readline() #reading data from serial
print(ar)

## Slide 10: Arduino code for task
int n1,n2;
String s1,s2;
volatile int state=1;
void setup()
{
pinMode(13,OUTPUT);
digitalWrite(13,LOW);
Serial.begin(9600);
}
void loop() {
if(Serial.available())
{
s1=Serial.readStringUntil(';'); //reads string until ‘;’
s2=Serial.readStringUntil(';');
n1=s1.toInt(); //converts string to int
n2=s2.toInt();
if(n1==5 && n2==12)
{ state=!state;
digitalWrite(13,state);
} }
Serial.print(s1);Serial.print(";");Serial.print(s2);Serial.println(";"); // writes the string to serial
}

## Slide 11: Output of task
You can see the on-board LED blinking on the Arduino
Apart from that you can see a series of strings printing on the python terminal
The letter ‘ b ’ represents bytes
The next part – ‘ 5;12. ’ is the data received
‘ \r\n ’ is end of line sequence
End of line sequences
Windows end of line sequence: \r\n
Unix end of line sequence: \n
Mac end of line sequence: \r

## Slide 12: ASCII chart
ASCII codes and their escape sequences
ASCII Name Description C Escape Sequence
nul null byte \0 (zero)
bel audible bell \a
bs backspace \b
ht horizontal tab \t
nl newline \n
cr carriage return \r