## Slide 1
Polling

## Slide 2
What is Polling?
The state of continuous monitoring is known as polling.
The microcontroller keeps checking the status of other devices; and while doing so, it does no other operation and consumes all its processing time for monitoring.
This can be accomplished by using the loop function in the arduino language
The following code gives an example of how we can use buttons with polling
However the arduino can only monitor the state of the button if we use this method

## Slide 3
int ledPin = 13; // choose the pin for the LED
int inPin = 7; // choose the input pin (for a pushbutton)
int val = 0; // variable for reading the pin status
void setup() {
pinMode(ledPin, OUTPUT); // declare LED as output
pinMode(inPin, INPUT); // declare pushbutton as input
}
void loop(){
val = digitalRead(inPin); // read input value
if (val == HIGH) { // check if the input is HIGH (button released)
digitalWrite(ledPin, LOW); // turn LED OFF
}
else {
digitalWrite(ledPin, HIGH); // turn LED ON
}
}
Using buttons with polling

## Slide 4
INTERRUPTS

## Slide 5
What are interrupts?
An interrupt is a signal from the micro-controller that requires the microcontroller to stop and figure out what to do next.
Almost all personal (or larger) computers today are interrupt-driven - that is, they start down the list of computer instructions in one program (perhaps an application such as a word processor) and keep running the instructions until either (A) they can't go any further or (B) an interrupt signal is sensed.
After the interrupt signal is sensed, the computer either resumes running the current program or begins running another program

## Slide 6
Here are some important features about interrupts −
Interrupts can come from various sources. In this case, we are using a hardware interrupt that is triggered by a state change on one of the digital pins.
Most Arduino designs have two hardware interrupts (referred to as "interrupt0" and "interrupt1") hard-wired to digital I/O pins 2 and 3, respectively.
You can define a routine using a special function called as “Interrupt Service Routine” (usually known as ISR).
You can define the routine and specify conditions at the rising edge, falling edge or both. At these specific conditions, the interrupt would be serviced.
It is possible to have that function executed automatically, each time an event happens on an input pin.

## Slide 7
Types of Interrupts:
There are two types of interrupts −
Hardware Interrupts − They occur in response to an external event, such as an external interrupt pin going high or low.
Software Interrupts − They occur in response to an instruction sent in software. The only type of interrupt that the “Arduino language” supports is the attachInterrupt() function.
Arduino only supports hardware interrupts

## Slide 8
By using interrupts to set up the buttons we can allow the micro controller to do something else while also simulataneously monitoring the buttons.
Furthermore we can setup the interrupt to trigger on either of the edges giving us more control with our code
In the arduino we have 2 external interrupts and 23 pin change interrupts
The difference between the two is that external interrupts can be configured to be triggered either on the rising or the falling edge or on both
However the ppin change interrupts trigger on both the edges
The following slide has the code required for the arduino using the external interrupt on pin two of the arduino

## Slide 9
The syntax for adding interrupts in arduino is :
attachInterrupt(digitalPinToInterrupt(“pin”),ISR,mode);
Here pin is the digital pin you wish to attach an interrupt to
ISR – is the “Interrupt Service Routine”
it is the code that you want to run when the interrupt is triggered
Mode
Mode is the mode of the interrupt you are setting up
INTERRUPTS IN ARDUINO
This function does’nt return a value

## Slide 10
Modes of interupts
The mode of an interrupt defines when the interrupt is triggered
1)RISING for rising edge 2)FALLING for falling edge
3)CHANGE for any change 4)LOW for if pin is low 5)HIGH for if pin high
However high is supported by only a few boards like Duw,zero,MKR100
etc
Rising edge
Falling edge
Low state
high state

## Slide 11
int pin = 2; //define interrupt pin to 2
volatile int state = LOW; // To make sure variables shared between an ISR
//the main program are updated correctly,declare them as volatile.
void setup() {
pinMode(13, OUTPUT); //set pin 13 as output
attachInterrupt(digitalPinToInterrupt(pin), blink, CHANGE);
//interrupt at pin 2 blink ISR when pin to change the value
}
void loop() {
digitalWrite(13, state); //pin 13 equal the state value
/*
any other code here
*/
}
void blink() {
//ISR function
state = !state; //toggle the state when the interrupt occurs
}
INTERRUPTS IN ARDUINO